## Slide 1: Femtosecond Laser Good, Bad & Ugly
Gautam Mishra, MD - Pro
  Harrisburg, PA
Joseph LoCascio, MD – Con
  Huntington, WV
David Faris, MD - Moderator
  Bridgeport, WV

## Slide 2: Femtosecond Laser Background
Femtosecond (FS) laser
  Infrared laser
  Wavelength of 1053 nm (Visible light – 400 to 700 nm)

## Slide 3: Femtosecond Laser Background
FS laser, like ND:YAG laser works by producing photodisruption (or photoionization) of optically transparent tissue – such as the cornea, anterior capsule, or lens

## Slide 4: Femtosecond Laser Background
Application of either FS laser or Nd:Yag laser results in the generation of a rapidly expanding cloud of free electrons and ionized molecules.
The acoustic shock wave so generated results in disruption of the treated tissue.

## Slide 5: Femtosecond Laser Background
However, the two lasers differ significantly in the amount of collateral damage they cause:
  Nd:YAG laser has a pulse duration in the nanosecond range where as the FS laser has a pulse duration in the femtosecond range.
  Reducing the pulse duration reduces the amount of collateral tissue damage.

## Slide 6: Femtosecond Laser Background
Collateral Damage
  106 times less with FS laser (vs. Nd:Yag laser).
  FS laser safe for corneal surgeries which requite precision.

## Slide 7: Femtosecond Laser History
FS laser designed by Drs. Juhsaz and Kurtz at U. of Michigan in the early 1990’s.
Many different FS laser systems are available commercially:
  IntraLase (Abbott Medical Optics, Inc.)
  Femtec (20/10 Perfect Vision)
  Femto LDV (Ziemer Ophthalmic Systems)
  VisuMax (Carl Zeiss Meditec AG)
  WaveLight FS200 (Alcon Laboratories Inc.)
  VICTUS (Bausch & Lomb)
  LensSx (Alcon Laboratories Inc.)

## Slide 8: Femtosecond Laser History
The various laser systems differ in:
  Available applications
  Pulse energy and frequency
  Applanation surface (flat or curved)
  Laser delivery pattern (raster/zigzag or centrifugal/spiral)
  VICTUS

## Slide 9: Femtosecond Laser History
The technology has evolved significantly since the 1990’s
  Laser firing has increased from 10-kHz to 150-kHz in the fifth generation IntraLase FS system
  Femto LDV operates in the mHz firing rate range, rather than kHz.
  The higher frequency allows reduced flap creation time and lower energy per pulse – smoother corneal stromal bed.

## Slide 11: Femtosecond Laser Clinical Applications
FS laser has a wide range of applications in corneal refractive surgery
  LASIK flap
  Astigmatic keratotomy

## Slide 12: Femtosecond Laser Clinical Applications
Corneal Refractive Surgery
  Channel creation for implantation of intrastromal corneal ring segments
  Femtosecond lenticule extraction

## Slide 13: Femtosecond Laser Clinical Applications
Other
  Intrastromal presbyopic correction (INTRACOR)

## Slide 14: Femtosecond Laser Advantages in LASIK
Reduced incidence of flap complications like buttonholes, free caps, irregular cuts, etc.
Greater surgeon choice and controp over flap diameter and thickness, side cut angle, hinge position, and length.
Increased precision with improved flap safety and better thickness predictability.
Capability of cutting thinner flaps to accommodate thin corneas and high refractive errors.
Absence of moving parts.

## Slide 15: Femtosecond Laser Advantages in LASIK
Stronger flap adherence
Better contrast sensitivity
Decreased incidence of epithelial ingrowth
Less increased IOP
Less incidence of dry eyes
Lesser hemorrhage from limbal vessels

## Slide 16: Femtosecond Laser Disadvantages in LASIK
Flap creation takes longer than with microkeratome (newer high frequency FS laser have overcome this disadvantage).
Opaque bubble layer – diffusing into deeper layers of stroma.
Transient light sensitivity syndrome TLSS/Good acuity plus photosensitivity GAPP.
Microirregularities on the back surface of the flap – “rainbow glare”.
Photodisruption-induced microscopic tissue injury – may cause lamellar keratitis

## Slide 17: Femtosecond Laser In Cataract Surgery
Potential Applications
  Corneal incision formation
  Anterior capsulotomy
  Lens disruption

## Slide 18: Femtosecond Laser In Cataract Surgery
Limbal Relaxing Incisions (LRI’s)